BIRCH TECHNOLOGY INC

7-13F, No#79, Shin Tai Wu rd. sec.1, Hsichih, Taipei, Taiwan.

TEL: 886-2-2698-9596 (10 lines)

FAX: 886-2-2698-9597

http: www.birch.com.tw

PRP-085III Ethernet Receipt Printer.

PRP-085III Ethernet Receipt Printer is specifically designed  for high-volume network receipt printing applications such as kitchen printing. By utilize a 32-bit CPU and a printer head that can support up to 220 mm / sec. printing speed., it features high speed printing of receipts, logo, and bar codes,  The PRP-085's highly reliable thanks to its built-in top quality Japanese SEIKO printer head and cutter mechanism.

| General Specifications |
| --- |
| Graphic Printing | Support NV images Download |  |
| Printing Method | Thermal line printing |  |
| Print head speed: | 220 mm per second |  |
| Paper width | 79.5 mm plus/minus 0.5 mm |  |
| Print Columns | 576 dots per line |  |
| Dot Density | 203 dpi. (8 dots per mm.) |  |
| Print Character | ANK Character, Font A: 12*24 dots, Font B: 9*17 dots,Chinese/Japanese/Korean: 24*24 dots |
| Languages | PAN European Languages: English, French, Germay, Denmark, Spanish, etc... Asian languages: Japanese, Korean, Chinesse |
| Interface: | Parallel/Serial(RS232C)/USB/Ethernet/ |  |
| Cutter | Full or Partial cuts |  |
| Head reliability | 100 Km |  |
| Power Supply | DC 12V to 24V, 1A |  |
| Cash Drawer | DC 12V to 24V solenoid supported |  |
| Kitchen Printing | Supported |  |
| Paper Thickness | 0.06 to 0.08 mm |  |
| Supported Barcodes | mode:UPC-A/UC-E/JAN13(EAN13)/JAN8(EAN8)/ |
| Software Driver | Drivers:Win9x/WinME/ Win2000/WinNT/ WinXP |
| Printer Command | ESC/POS compatible |  |
| Ext. Dimension | 145 x 203 x 135 mm |  |